## Slide 1: Walan Specialty Construction Products, LLC – Public Hearing
November 20, 2018

## Slide 2: DAQ Air Permit Application Review Process
Received Application October 19, 2018
Public Notice October 28, 2018
Public Hearing November 20, 2018

## Slide 3: Project Summary
The proposed Facility will produce a fine slag material which is an additive for use in the construction industry.
Coarse slag will be dried using natural gas with proposed emissions within allowable limits.
The drying and grinding operations will be enclosed and will utilize a baghouse and other air pollution control equipment.

## Slide 4: Project Summary
Emissions – The process emissions will consist of particulate matter (PM) from materials handling and emissions from combustion of natural gas (PM, NOx, CO, SO2, VOC)
PM is controlled via baghouse, storage silos with bin vents, and dustless loadout chutes with cartridge filters.

## Slide 5: Project Summary
Potential to Emit (PTE) table
The emissions will be monitored using methods based on material processed and fuel usage.
Pollutant | Uncontrolled (lb/hr) | Controlled (lb/hr) | Annual PTE (tons/yr) | Requested Permitted (tons/year)
PM | 286.247 | 1.318 | 5.776 | 5.776
PM10 | 231.600 | 1.037 | 4.543 | 4.543
PM2.5 | 72.655 | 0.366 | 1.591 | 1.591
NOX | 0.724 | 0.724 | 3.171 | 3.171
CO | 0.608 | 0.608 | 2.664 | 2.664
SO2 | 0.004 | 0.004 | 0.019 | 0.019
VOC | 0.040 | 0.040 | 0.174 | 0.174

## Slide 6: DAQ Permitting
If Secretary approves the permit, then DAQ will issue construction permits that will:
  Meet strict air quality standards under the Federal and Delaware State regulations
  DAQ permits are supported by a detailed technical review and include permit conditions that will protect the environment and public health
  Contain permit conditions that may address concerns raised during the public hearing

## Slide 7: DAQ Permitting
If the construction permit is issued, DAQ will conduct a Construction-to-Operation inspection following construction
Following a successful C to O inspection, the company would receive an operating permit that will require:
  Monitoring
  Recordkeeping and
  Reporting
DAQ performs periodic compliance inspections

## Slide 8: DAQ Permitting
Normal permit conditions include:
  Require the plant and controls to meet strict emissions limits protective of human health and the environment
  Record operating data and keep the data for 5 years
  Report deviations from permitted conditions
  Opacity observations
  Maintain dust control plan

## Slide 9: Thank You