## Slide 1: Air Permit Application DNREC Public Hearing November 20, 2018
WALAN Specialty Construction Products, LLC

## Slide 2: Project Summary
Application status
History of application
Project provides ground granulated blast furnace slag (GGBFS)
Location (Port of Wilmington, Interstate, railroad, regional market, workforce)
GGBFS in demand
Currently no local source of GGBFS
Appropriate Zoning
1/3 mile to nearest residence
Minor air emissions source
Minimal risk -- Emissions comply with health based regulatory standards
Best available control technology (BACT)
No chemical additives
Newest equipment in industry
WALAN has 30 years of mineral grinding expertise
Value for Delaware – lower end user costs, tax base, local jobs, supports local businesses, Port

## Slide 3: Location: 501 Christina Avenue in Wilmington, DE

## Slide 4: Wilmington Location
Properly zoned - Waterfront Manufacturing W-1
Purpose. The W-1 waterfront manufacturing district provides areas where manufacturing and heavy industrial uses are well established and where there are suitable sites for such uses served by rail, water and highway networks. (Sec. 48-336.-W-1 district)
Surrounding parcels zoned for Waterfront Manufacturing and Light Manufacturing
Proximity to Port of Wilmington
Access to Interstate and rail
Access to trainable workforce
Regional market for material

## Slide 5: Ground Granulated Blast Furnace Slag (GGBFS) is:
  A portland cement substitute in concrete
  Increases strength and durability of concrete
  Odorless
  Being required in regional DOT funded projects and private construction
WALAN’s process grinds granulated blast furnace slag from sand–like grains to powder

## Slide 6: THE PROCESS – GBFS TO GGBFS

## Slide 7: Overview of our Process
Ground Granulated Blast Furnace Slag (GGBFS) Grinding Facility

## Slide 8: The Grinding Operation
New Gebr. Pfeiffer Vertical Roller Mill, modular system

## Slide 9: Product Storage Silos
After grinding, our finished product GGBFS will be stored in sealed silos with dustless loading spout
Source: https://www.indiamart.com

## Slide 10: Finished Product Transport
Enclosed bulk tanker trucks with sealed hatches will carry GGBFS, our finished product, out of the plant

## Slide 11: Local Truck Routes to Port, Interstate

## Slide 12: Route to Local Clients

## Slide 13: Projected Air Emissions
Pollutant | Maximum Controlled Emission Rate (lbs/hour) | Projected Annual Air Emissions (tons/year) | New Castle County Major Source Thresholds (tons/year)
Particulate Matter (PM) | 1.318 | 5.776 | --
PM10 | 1.037 | 4.543 | 100
PM2.5 | 0.366 | 1.591 | 100
Sulfur Oxides (SOx) | 0.004 | 0.019 | 100
Nitrogen Oxides (NOx) | 0.724 | 3.171 | 25
Carbon Monoxide (CO) | 0.608 | 2.664 | 100
Total Volatile Organic Compounds (VOCs) | 0.040 | 0.174 | 25
Identified as natural minor source of emissions by DNREC

## Slide 14: Emission Controls
  Best Available Control Technology (BACT)
    Baghouses and bin vents to capture particulate matter from grinding mill and silos
    Dustless load from silos to trucks
  Best Management Practices:
    Maintaining moisture content of material
    Stockpile tarping
    Delivery truck beds entering facility will be covered
    Trucks on paved surfaces
    Pavement sweeping
    Speed limits
    Curtained truck entrances/exits beneath silos
    Daily facility inspection and maintenance
    Regular inspection/maintenance of equipment
    Employee training
    Daily record keeping

## Slide 15: Emissions Comparison with National Health Standards
Pollutant | Predicted Pollutant Concentration (mg/m3) (1) | Wilmington MLK 2016 Air Quality Monitoring Results (mg/m3) (2) | Combined Total Concentration (mg/m3) (3) | National Ambient Air Quality Standards (mg/m3) (4)
PM10 | 6.61 | 14.2 | 20.81 | 150
PM2.5 | 1.96 | 9.2 | 11.16 | 12
NOx | 1.33 | 22.56 | 23.89 | 188
SOx | 0.0073 | 13.1 | 13.11 | 196.5
CO | 1.11 | 1832 | 1,833.11 | 10,000
Total substance concentrations in micrograms per cubic meter (mg/m3) were calculated using the Screen3 dispersion modeling program. Models were created for each emissions stack.
(2) Air quality results published by DNREC in 2016 for the Wilmington MLK monitoring station.
(3) The maximum 1‐hour concentrations from the models added to the Wilmington MLK air quality monitoring station results from 2016 gives an approximate combined air quality for comparison.
(4) The Environmental Protection Agency publishes the National Ambient Air Quality Standards (NAAQS). The primary standards consider the health of sensitive receivers (asthmatics, elderly, children, etc.)

## Slide 16: Proximity of Site to Residential Areas

## Slide 17: Photo 1 - View of Site from I-495 Bridge

## Slide 18: Photo 2 - View of Site from Christina Avenue

## Slide 19: Photo 3 - View from Site Toward Southbridge and Hicks Park

## Slide 20: Photo 4 – Opposite Side of Christina Avenue

## Slide 21: Photo 5 - View from Hicks Park

## Slide 22: Company background
For over 30 years, a corporate affiliate of WALAN has been in the mineral grinding business
  Iron ore grinding plant in Adrian, PA, servicing clients across the globe since 1982
  Iron chromite grinding plant in Claysburg, PA, operating since 1987
  Performance with consideration for the health and safety of employees, partners, neighbors, and customers
Goals for the future in Wilmington
  Serve DE and regional market with sustainable, alternative material for construction
  Reduce costs for local business and construction projects
  Utilize transportation infrastructure
  Employ qualified local residents
  Be a good steward and neighbor as done in Pennsylvania

## Slide 23: Community engagement
Company heard questions/concerns at previous public hearing
Engaged local stakeholders -- civic leaders and organizations, elected officials, business interests
Goals were to share information about project, answer questions, address concerns
  Attended:
    Oakmont Civic Association Meeting
    Route 9 Corridor All Civic Associations Meeting

## Slide 24: Response to community concerns
Modified truck routes to eliminate traffic through residential areas
Added tarp coverage of stockpiled material to dust control plan
Conducted cumulative impacts analysis to assess potential impact on community from air emissions
Bring practice of community support to DE that has been part of affiliate company culture in PA

## Slide 25: Thank you